## Slide 1: Precipitation products comparison over European and African areas: methodology and data used
Marco Petracca, Silvia Puca
DPC (Italy)
Jan Kanak
SHMU (Slovakia)
and Quality Assessment Cluster
Marco Petracca

## Slide 2: Outline
Quality Assessment activities (Q.A.)
Precipitation Product Validation Group (PPVG)
Precipitation products
Reference precipitation data
Validation Methodology (over Europe and Africa)
Results and conclusion

## Slide 3: Quality Assessment activities
Validation activities have particular relevance towards end-users of the products.
There are two main requirements according to the specific use of the products:
1- the direct use by human operators monitoring in real time the Hydrological situation for taking decision
2- the direct use by hydrological numerical models to provide run off information
In order to accomplish such requirements, two dedicated clusters were designed to elaborate the direct end-user quality assessment service.

## Slide 4: Quality Assessment activities
To assess the benefits of the satellite-derived data on practical hydrological applications
To monitor the product quality

## Slide 5: Quality Monitoring and Assessment Service
the Quality Monitoring and Assessment service is responsible to:
• monitor the progress in product quality;
• provide validation service to end-users;
• provide ground data service inside the project;
• investigate the H SAF product impact in end-user applications.
The cluster is coordinated by the Italian Civil Protection Department (DPC)

## Slide 6
Precipitation Product Validation Group (PPVG)
The Precipitation Product Validation Group (PPVG) is composed of experts from the National Meteorological and Hydrological Institutes of 8 European countries. The PPVG uses ground data for quality assessment of precipitation products, following the same methodology.
Country | Institutes
Belgium | RMI
Bulgaria | NIMH
Germany | BfG
Hungary | OMSZ
Italy | DPC, UniBo
Poland | IMWM
Slovakia | SHMU
Turkey | ITU, METU,TSMS

## Slide 7: Op Precipitation Products PMW-based
 | H01 new rel. (P-IN-SSMIS) | H02B (P-IN-MHS) | H18 (P-IN-ATMS)
Coverage | Strips of ~1700 km swath crossing the MSG 0° extended Full Disk area | Strips of ~2250 km swath crossing the MSG 0° Full Disk area | Strips of ~2250 km swath crossing the MSG 0° extended Full Disk area
Cycle | Up to 6 passes/day | Up to 8 passes/day | Up to 4 passes/day
Spatial Resolution | ~13.2 x 15.5 Km2 (SSMIS 91.6 GHz channel resolution) | Corresponds to the nominal resolution of MHS, vaying from 16 x 16 Km2 to 26 x 52 Km2 | Corresponds to the nominal resolution of ATMS, vaying from 15.82 x 15.82 Km2 to 26 x 52 Km2
Timeliness | 150 minutes from observing time | 30 minutes from observing time | 30 minutes from observing time
physically-based Bayesian approach
Neural network approach
Dissemination via EUMETCAST
NetCDF
H01
H02
H18

## Slide 8: Op Precipitation Products SEVIRI-based
Marco.Petracca@protezionecivile.it (DPC)
8
 | H03B (P-IN-SEVIRI) | H05B (P-AC-SEVIRI) | H15A (P-IN-SEVIRI-CO)
Coverage | MSG 0° Full Disk area | MSG 0° Full Disk area | H SAF area extended up to higher latitudes
Cycle | 15 minutes – every new SEVIRI image | 3-6-12-24h cumulated every three hours | 15 minutes – every new SEVIRI image
Spatial Resolution | dependent of SEVIRI IFOV. In average: Res 8 Km; Sampling: 5 Km | dependent of SEVIRI IFOV. In average: Res 8 Km; Sampling: 5 Km | dependent of SEVIRI IFOV. In average: Res 8 Km; Sampling: 5 Km
Timeliness | within 15 minutes from the end of acquisition | 15 minutes after synoptic hours (0-3-6...21 UTC) | within 15 minutes from the end of acquisition
Blending technique
Dissemination via EUMETCAST
NetCDF
H03
H05
H15

## Slide 9: Operational Precipitation Products
Operations Readiness Review (ORR)
The transition from “In development” to ”Pre-operational” to “Operational” is gradual, as long as sufficient validation becomes available. Related milestones and processes (reviews) are organized depending on the progress.
Operation Readiness Review (ORR) aimed to assess the validation result and readiness to deliver the Products
The Operation Reviews (OR) yearly planned involves all the operational / pre-operational products.
Operations Review (OR)
? When and how are the products validated ?

## Slide 10: Validation over Europe
European area
European ground data:
radars and raingauges

## Slide 11: European ground data: raingauges
More than 8,000 rain gauges
Country | Total number of gauges | Average minimum distance (km)
Belgium | 92 | 15.2
Bulgaria | 123 | 25.2
Germany | 2299 | 12.9
Hungary | 270 | 17.0
Italy | 2934 | 11.3
Poland | 540 | 24.0
Slovakia | 911 | 13.6
Turkey | 1235 | 26.5
TOTAL | 8404 | 
Most of the gauges used in the National networks by the validation Groups are of the tipping bucket type, which is the most common device used worldwide to have continuous, point-like rain rate measurement. The German network, and a part of the Bulgarian network, as an example, are equipped by precipitation weighing gauges, that allow continuous precipitation (both solid and liquid) measurements with higher accuracy.
Minimum detectable rain ≥ 0.1 mm
Available output format
ASCII
Typical time resolution
1 hour

## Slide 12: European ground data: radars
71 C-band radars
Country | Total number of radar | Average minimum distance (km)
Belgium | 1 | -
Bulgaria | - | -
Germany | 16 | 163
Hungary | 4 | 190
Italy | 22 | 141
Poland | 8 | 186
Slovakia | 4 | 137
Turkey | 16 | 253
TOTAL | 71 | 
Time resolution
5 – 60 minutes
Minimum detectable rain rate
≥ 0.01 mm/h
Output formats
HDF5, NetCDF, …
Institutes involved in the PPVG declared the system are kept in a relatively good status and all of them apply some correction factors in their processing chain of radar data. Only the radar data which passes the Quality Check of the owner Institute are used by the PPVG for validation activities.

## Slide 13: Validation methodology over Europe
1. GROUND DATA
Spatial interpolation (GRISO)
Quality check and filtering
2. TEMPORAL-SPATIAL MATCHING
Upscaling to the product grid
3. STATISTICAL (CONTINUOUS AND MULTI-CATEGORICAL) SCORES
Precipitation classes:
Light [0.25≤RR (mm/h) <1.0 ]
Moderate [ 1.0≤ RR (mm/h) <10.0]
Heavy [ RR (mm/h) ≥10.0]
All [ RR(mm/h) ≥ 1.0 ]
Surface types:
Sea
Land
Coast
Overall
Time intervals:
Monthly
Seasonal
Yearly
Precipitation phases:
Liquid
Solid
Mixed
All
This comparison methodology is performed by the Unique Common Code (UCC) for all (8) participating countries (PPVG)
<- the validation is performed over the satellite grid. Only the reference data is degraded and not the satellite data. This is to evaluate the product at the same resolution as the data released.

## Slide 14: Summary results over Europe
How to objectively determine if a product satisfy User Requirements?
Fractional Standard Error (FSE) %
FSE = [RMSE / <obs>] *100%
REQUIREMENTS (FSE%) |  | 
OPTIMAL | TARGET | THRESHOLD
100 | 150 | 200

## Slide 15: Summary results over Europe
Chart: Precipitation products FSE% annual trend
| 2017 | 2018 | 2019 | 2020
P-IN-SSMIS | 144 | 146 | 133
P-IN-MHS | 118 | 117 | 125
P-IN-SEVIRI | 138 | 129 | 148
P-AC-SEVIRI | 147 | 133 | 187
P-IN-SEVIRI-CO | 182 | 145 | 155

## Slide 16: Comparison over Africa
African area
Reference ground data:
radars and/or raingauges
Satellites

## Slide 17: Available precipitation data over Africa
Few gauges, very few weather radars
Non-homogeneous extension over the whole Africa
Daily or monthly data of climatological interest and not hourly or sub-hourly
Precipitation datasets not independent by the products to be validated
Data only on land areas

## Slide 18: Associate Scientist activity result
«…it can be establish that 2A-DPR NS V05 can be used to verify the H03 (P-IN-SEVIRI) rainfall estimations where the ground radars are not available, as is the case for most of the African territory. This is more true for light to moderate precipitation, whereas for heavy precipitation DPR products should be used with more caution, due to the underestimation of DPR with respect the reference and to the scarce data of heavy precipitation sampled by the ground-based radars.»

## Slide 19: Dual-frequency Precipitation Radar (DPR)
prEs Precipitation Estimated on Surface
2 product types (K-band only / Combined [DPR] Product)
3 Scan modes (NS, MS and HS)
Features | KuPR | KaPR
Frequency | 13.6 GHz | 35.5 GHz
Swath Width | 245 km | 120 km
Spatial Resolution | 5.2 km (Nadir @ 407 km) | 
Beam Width | 0.71° (Center Beam) | 
Beam Number | 49 Normal Scan, NS | 49: 25 in matched beams (MS) + 24 in interlaced scans (HS)
Min. measur. RR | 0.5 mm/h | 0.2 mm/h
Cross T. Scan Angle | ±17° | ±8.5°

## Slide 20: Comparison methodology over Africa
Intersection [temporal and spatial GPM vs NOAA/METOP and MeteoSat acquisitions]
Downscaling [regular grid 0.5°]
Comparison [pixel-based]
Results
20
Statistical scores
(events, monthly, seasonal, yearly)
For different precipitation classes
(≥ 1 mm/h; ≥ 5 mm/h ; ≥ 10 mm/h)
For different surface types
(sea, land, coast)
For different geographical areas
(Africa, Europe, Ocean)

## Slide 21: Summary results over Africa
Comparison results over 12 months (2017-2018)
Full validation results available on ORR report
H18 (P-IN-ATMS) is OPERATIONAL since 20/02/2020

## Slide 22: Summary results over Africa
Comparison results over 12 months (2017-2018)
H18 (P-IN-AMSU) is OPERATIONAL since 20/02/2020
Full validation results available on ORR report
FSE=108%

## Slide 23: Conclusion
Quality assessment service monitors the progress in product quality (OR)
ORR aimed to assess the readiness to deliver a product (-> operational or pre-operational)
Products successfully reviewed are available to end-users (EUMETcast, FTP)
Validation over Europe respect to ground precipitation data as reference
Comparison over Africa respect to DPR products (AS 2017)
FSE score is an indicator of how good a product is for users' purposes (User Requirement)
All operational precipitation products fully satisfy the User Requirements (FSE% between target and optimal);

## Slide 24
http://hsaf.meteoam.it/
Thank you for your attention !
Question?
Contact us!
Marco.Petracca@protezionecivile.it
Silvia.Puca@protezionecivile.it
@HydroSAF
RENEWED
SOON